## Slide 1: BRIDGE FAILURES IN ALBERTA

## Slide 2: Introduction
Bridges are inspected for three primary reasons
  safety of bridge system
  maintenance of bridges
  management of the bridge system
Inventory or management of the system can be just as important as safety and maintenance

## Slide 3: Need to Know
Which bridges are:
  substandard and not adequate to carry full legal loads
  susceptible to flooding
  high priority for replacement

## Slide 4: Cause of Failure
70% of failures are caused by factors related to water flow
  scouring of piers
  undermining of the support elements
Structural failure
  element failure due to excess load or material deterioration
Lack of knowledge or good judgment
  Operation
  Construction
  Design

## Slide 5: Contributing Factors
Structural engineering is a science
  applied truckloads are known
  material behavior is known and can be accurately predicted
  everything can be accurately calculated and predicted
River engineering is more of an art
  the effects of a flood cannot simply be calculated
  the effects of Mother Nature are not easily predicted
  the velocity and angle of flow, the duration of flooding, etc.

## Slide 6: Bear Creek 84 Ave in Grand Prairie
SPCSP HE 5.5 x9m
Installed in 1973
Total collapse of the structure in 1988
No inspection after installation
Notes: 5

## Slide 7: Bear Creek on 84 Ave in Grande Prairie
Structure on 84 Avenue Grande Prairie
Notes: 6

## Slide 8: Bear Creek on 84 Ave in Grande Prairie
Total collapse of culvert. Only headwall intact

## Slide 9: Bear Creek on 84 Ave in Grande Prairie
Inside collapsed culvert

## Slide 10: Bear Creek on 84 Ave in Grande Prairie
Outlet of culvert

## Slide 11: Bear Creek on 84 Ave in Grande Prairie
Backfill characteristics

## Slide 12: Bear Creek on 84 Ave in Grande Prairie
Water and sewer line in embankment

## Slide 13: Beaver Ranch Creek 58 East of Vermilion
SPCSP HE 4.8 x 7.3
Installed in fall of 1987
Extensive deformation in 1988
Total collapse in 1989 while fill being removed for repair of culvert

## Slide 14: Beaver Ranch Creek – 58 East of Vermilion
Outlet showing intact end treatment

## Slide 15: Beaver Ranch Creek – 58 East of Vermilion
Inlet with culvert still connected to headwall

## Slide 16: Beaver Ranch Creek – 58 East of Vermilion
Overview of culvert inlet

## Slide 17: Weed Creek Highway 39 Near Thorsby
Arch culvert
Constructed in 1960
Washed out July 3rd, 1990.

## Slide 18: Weed Creek – Hwy 39 Near Thorsby
Concrete arch culvert in 1989

## Slide 19: Weed Creek – Hwy 39 Near Thorsby
Water on U/S end up to shoulder of road

## Slide 20: Weed Creek – Hwy 39 Near Thorsby
Hole in side slope of D/S side

## Slide 21: Weed Creek – Hwy 39 Near Thorsby
Water now coming out of D/S fill

## Slide 22: Weed Creek – Hwy 39 Near Thorsby
Road gone

## Slide 23: Weed Creek – Hwy 39 Near Thorsby
Upstream Inlet

## Slide 24: Weed Creek – Hwy 39 Near Thorsby
D/S Outlet

## Slide 25: Weed Creek – Hwy 39 Near Thorsby
Centre section of the culvert

## Slide 26: Weed Creek – Hwy 39 Near Thorsby
Erecting 8.5 m SPCSP

## Slide 27: Weed Creek – Hwy 39 Near Thorsby
U/S inlet of new culvert

## Slide 28: BF 77496 – Hwy 40 Lineham Creek, Kananaskis
4.3M diameter Structural Plate Ellipse (SPE) culvert installed in 1983.
53M invert length.
9.1M road to streambed height.
Washed out during 2013 flood event.

## Slide 29: BF 77496 – Looking D/S at scale of washout (30m wide vs. 4.3M pipe).

## Slide 30: BF 77496 – Drift blockage across inlet and heaved barrel.

## Slide 31: BF 77496 – Inlet blockage and barrel heave

## Slide 32: BF 77496 – Outlet and barrel floor folded and heaved nearly to roof

## Slide 33: BF 77496 – Replaced in 2015 with new 8-14-8 M SLW girder bridge

## Slide 34: Red Willow River Local Road near Rio Grande
150’through truss built in 1927
Bridge posted for 17 tons
Bridge collapsed in 1977
Failure of rotten abutment corbel

## Slide 35: Red Willow River on Local Road near Rio Grande
Collapsed Bridge

## Slide 36: Red Willow River on Local Road near Rio Grande
Abutment end of the bridge showing timber decking etc.

## Slide 37: Red Willow River on Local Road near Rio Grande
Abutment end of truss dropped and buckled the bottom chord

## Slide 38: Castle River Bridge Local Road West of Pincher Creek
built in 1951 designed by a consultant in Toronto
Concrete T girder in poor condition in 1961
replaced in 1981

## Slide 39: Castle River Bridge on Local Road West of Pincher Creek
Recorded crack pattern in 1964

## Slide 40: Castle River Bridge on Local Road West of Pincher Creek
Bridge condition in 1979 (28 years old)

## Slide 41: Castle River Bridge on Local Road West of Pincher Creek
Shear crack in girder and efflorescence from cracks

## Slide 42: Castle River Bridge on Local Road West of Pincher Creek
Shear crack at girder end

## Slide 43: Castle River Bridge on Local Road West of Pincher Creek
Removing the bridge in August 1980

## Slide 44: Castle River Bridge on Local Road West of Pincher Creek
Bridge Down

## Slide 45: Castle River Bridge on Local Road West of Pincher Creek
Bridge remains

## Slide 46: Simonette River Bride Forestry Trunk Road (South of Debolt)
Timber and Bailey built in 1960 deck to s/b 3m
1982, 2 through trusses 60.96m 9m deck to s/b
Washed out in 1987 (Tornado Flood)
Rebuilt in 1988

## Slide 47: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Forestry bridge built in 1960, 380 ft. long bridge

## Slide 48: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Forestry Double Bailey, chord reinforced 2 @ 100 ft.

## Slide 49: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Bridge built in 1982, 122m bridge

## Slide 50: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Forestry road with river in floor, 1987

## Slide 51: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Truss partly under water

## Slide 52: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Drift jamming under bridge

## Slide 53: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Bridge floating and starting to shift

## Slide 54: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Bridge starting to move laterally

## Slide 55: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Bridge floating downstream

## Slide 56: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
One span tipped in middle channel and other one around near shore.

## Slide 57: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
Bridge gone.

## Slide 58: Simonette River Bridge on Forestry Trunk Road (South of Debolt)
New bridge.

## Slide 59: Beaverhill Creek Local Road North of Lamont
3-28’ Precast Concrete
Constructed in 1959
North pier cap failure in August 1980

## Slide 60: Beaverhill Creek on Local Road North of Lamont
Local road with gravel truck pup remaining on bridge

## Slide 61: Beaverhill Creek on Local Road North of Lamont
Pup tandem axle in hole left by dropped girder

## Slide 62: Beaverhill Creek on Local Road North of Lamont
Sheared timber cap. One girder hung up on pile.

## Slide 63: Beaverhill Creek on Local Road North of Lamont
Failed pier cap

## Slide 64: Beaverhill Creek on Local Road North of Lamont
Failed pier cap with girder dropped to pile top level.

## Slide 65: Beaverhill Creek on Local Road North of Lamont
Bottom of cap with piled punching (North pier)

## Slide 66: Little Smoky Bridge SH 744
Constructed in 1954
150 span failed in 1980 by cat and blade on high boy

## Slide 67
Severed batter post U7- L8
Little Smoky Bridge on SH 744
Broken hanger U7 - L7 and
first diagonal U7 - L6

## Slide 68: Little Smoky Bridge on SH 744
Members L6 – U5 and U5 – L5 buckeled

## Slide 69: Little Smoky Bridge on SH 744
Inside of truss sagged 2’-0 leaning 10”

## Slide 70: BF 1153 – Hwy. 22 over Oldman River near Lundbreck
3 span Type PO girders on concrete substructure -built 1959.
Span lengths of 20.7 – 29 – 29 M.
Typ. Sliding Plate Bearing with Self-Lubricating Bronze Plates.
Expansion Bearings at P1 and P3. Deck height is 18.5M.
Routine Level 1 BIM inspection of December 2015 noted frozen bearings at the west end of P1 under Span 1 - G1 and G2.
Significant portion of concrete pier cap under G1, G2 bearings had failed due to induced stresses into pier from frozen bearings resulting in G1 un-supported and near collapse.
Lane above immediately closed and truck traffic detoured.
Subsequent BIM Advisory bulletin #3 issued January 20, 2016.

## Slide 71: BF 1153 – Hwy. 22 Oldman River 21-29-29-27m Type PO Girders – Deck Height 19m - 1959

## Slide 72: BF 1153 – Standard Drawing S-701

## Slide 73: BF 1153 – Failed concrete at west end of P1 from frozen bearings under G1, G2. G2dbreck

## Slide 74: BF 1153 – Failed pier concrete and un-supported bearing under Sp. 1-G1.

## Slide 75: BF 1153 – 30mm drop in rail and curb over Sp.1-G1.

## Slide 76: BF 1153 – Neoprene Pads & Widened/Strengthened Pier Caps

## Slide 78: Questions?