## Slide 1: STRUCTURAL CONSIDERATIONS FOR TRUSSES

## Slide 2: Introduction
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
Pratt Truss
Notes: Truss members carry axial loads (tension and compression), rather than bending like beams/girders.
Floorbeams and stringers carry in bending
Advantages because design is simply on the cross section area, with buckling considerations. Small members.
Why else would we use truss bridges?
Why don’t we today?

## Slide 3: Truss Types
Three types of trusses in Alberta:
  Pony trusses
  Through trusses
  Deck trusses
Traffic loads are transferred to the trusses by a floor system.
Notes: Pony truss. No vertical restrictions for traffic. Can’t carry heavy loads. Top chord is not braced
Through truss. Has vertical restrictions. Can carry heavy loads
Deck truss. No vertical restriction. Can carry heavy loads. Lots of superstructure below deck. (clearance below)

## Slide 4: Floor System
Stringers supported
by Floor Beams
Truss Panel Point
Wind Bracing
Floor Beams supported by
Trusses at Truss Panel Points
Deck supported by
Stringers
Notes: Stringer to floorbeams to panel points.
Truss analysis is a discrete “point”

## Slide 5: Pony Truss
Wind Bracing
Floor Beams

## Slide 6: Through Truss
Upper Wind Bracing
System
Batter Posts
Portal Brace

## Slide 7: Portal Brace & Batter Posts
Batter Posts
Portal Brace
Floor Beam
Wind Load
Notes: These are axially loaded members either.

## Slide 8: Deck Truss
Lower Wind Bracing
System

## Slide 9: Deck Truss – Wind Bracing
Upper Wind
Bracing System
Lower Wind
Bracing System
Diagonal
Bracing
Main Truss
Members

## Slide 10: Truss Configurations
The way truss members carry loads depends on the configuration of the truss.
Most trusses in Alberta are either Pratt or Warren trusses.

## Slide 11: Pratt Truss
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
Top Chord
Bottom Chord
Vertical
Diagonal
Crossed Diagonals
M1

## Slide 12: Warren Truss
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
Top Chord
Bottom Chord
Vertical
Diagonal
L8
U7

## Slide 13: Truss Curvature
Tension
Bottom Chord
Top Chord
Notes: Tension and compression
Buckling of top chord
Cracks in bottom chord
Be concerned

## Slide 14: Loads in Diagonals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
M1
Notes: Loads applied to the right

## Slide 15: Loads in Diagonals
U2
U3
L2
L3
This side of the panel is being pulled down by the loads to the right
This side of the panel is being held up by the left support
Notes: tension

## Slide 16: Loads in Diagonals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
M1

## Slide 17: Loads in Diagonals
U2
U3
L2
L3
This side of the panel is being pulled down by the loads to the left
This side of the panel is being held up by the right support
Notes: compression

## Slide 18: Loads in Diagonals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
M1

## Slide 19: Loads in Diagonals
U2
U3
L2
L3
This side of the panel is being pulled down by the loads to the right
This side of the panel is being held up by the left support
Notes: Tension and compression

## Slide 20: Loads in Diagonals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
L8
U7

## Slide 21: Loads in Diagonals
U2
U3
L2
L3
This side of the panel is being pulled down by the loads to the right
This side of the panel is being held up by the left support
Notes: compression

## Slide 22: Loads in Diagonals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
L8
U7

## Slide 23: Loads in Diagonals
U2
U3
L2
L3
This side of the panel is being pulled down by the loads to the left
This side of the panel is being held up by the right support
Notes: tension

## Slide 24: Summary – Loads in Diagonals
Diagonals that slope away from the nearest support as they approach the bottom chord are primarily tension members.
Some diagonals near the center of the truss may go into compression.
Diagonals that slope towards the nearest support as they approach the bottom chord are primarily compression members.
Crossed diagonals are tension members.
Notes: They can all be both
Crossed are tension because buckling of same member will be significantly less than tension of other member

## Slide 25: Summary – Loads in Diagonals
Diagonals |  | 
Slope away from nearest support approaching BC | Slope towards nearest support approaching BC | Crossed
Tension | Compression | Tension

## Slide 26: Loads in Verticals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
M1

## Slide 27: Loads in Verticals
U2
L2
Top chord in compression
Bottom chord in tension
Vertical
Diagonals in tension
Notes: compression

## Slide 28: Loads in Verticals
U2
L2
Top chord in compression
Bottom chord in tension
Vertical
Diagonals in compression
Notes: tension

## Slide 29: Loads in Verticals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
M1

## Slide 30: Loads in Verticals
U1
L1
Bottom chord in tension
Vertical
Diagonal
Batter Post
Notes: tension

## Slide 31: Loads in Verticals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
M1

## Slide 32: Loads in Verticals
U1
L1
Bottom chord in tension
Vertical
Diagonal
Batter Post

## Slide 33: Loads in Verticals
L0
L1
L2
L3
L4
L5
L6
L7
U1
U2
U3
U4
U5
U6
L8
U7

## Slide 34: Loads in Verticals
U2
L2
Top chord in compression
Vertical
Diagonal
Diagonal

## Slide 35: Summary – Loads in Verticals
Verticals connected to diagonals at both ends will be in compression if the diagonals are in tension and in tension if the diagonals are in compression.
Verticals connected to diagonals at the top chord only will be in tension for pony and through trusses and will be unloaded for deck trusses.
Verticals connected to diagonals at the bottom chord only will be in compression for deck trusses and will be unloaded for pony and through trusses.
Notes: Explain deck truss examples for warrant truss. Bottom chord and top chord can only take axial loads. Or it would be so flexible that it’ll be the diagonals alone that carry the load. It’s got to get to those diagonals though in order to carry.
Draw example on whiteboard of warren truss

## Slide 36: Summary – Loads in Verticals
Vertical Connected to |  |  |  |  | 
Diagonals at both ends |  | Diagonals at top chord |  | Diagonals at bottom chord | 
Diagonals in tension | Diagonals in compression | For pony & through trusses | For deck truss | For pony & through trusses | For deck truss
Compression | Tension | Tension | Zero | Zero | Compression

## Slide 37: Summary – Loads in TC, BC & BP
Top chords are in compression.
Bottom chords are in tension.
Batter posts are in compression.

## Slide 38: Steel Sections
Single Angle
Double Angles
Four Angles
Channel
Double Channel
W-Section

## Slide 39: Tension Member

## Slide 40: Compression Member
Misalignment of Member

## Slide 41: Compression Member
Bent Member

## Slide 42: Compression Member
Rippling of Plate

## Slide 43: Compression Member
Rippling of Plate

## Slide 44: Compression Member
Bracing

## Slide 45: Class Exercise
U0
U1
U2
U3
U4
U5
U6
U7
U8
L0
L1
L2
L3
L4
L5
L6
L7
L8
1
2
3
4
Notes: 1 – Compression
2 – Tension
3 – Tension
4 - Zero

## Slide 46: Class Exercise
U1
U2
U3
U4
U5
U6
U7
U8
L0
L1
L2
L3
L4
L5
L6
L7
L8
L9
5
6
7
8
9
10
Notes: 5 – Tension
6 – Tension
7 – Compression, oh wait Tension
8 – Compression
9 – Compression
10 - Tension

## Slide 47: Truss Loads
U1
U2
U3
U4
U5
U6
U7
L0
L1
L2
L3
L4
L5
L6
L7
L8
5
5
10
10
10
10
10
10
10
40
40
60°
60°
Notes: Start at L0
Sum forces in y. L0-U1 only member with y-component. Therefore can solve
Sum forces in x. Use L0-U1 to get L0-L1
Move to L1
Sum forces in y. L1U1 = 0
Sum forces in x. L1L2=L0L1
Move to U1
Sum forces in y. Get U1L2
Sum forces in x. Use U1L2 to get U1U2

## Slide 48: Truss Loads
U1
U2
U3
U4
U5
U6
U7
L0
L1
L2
L3
L4
L5
L6
L7
L8
40.4
40.4
34.6
34.6
34.6
34.6
46.2
46.2
20.2
20.2
20.2
20.2
43.3
43.3
43.3
43.3
17.3
17.3
28.9
28.9
5.8
5.8
0
0
0
10
10
10
10
Compression Force
Tension Force
Notes: Uniform load across structure. Normal loading condition
BC – Large tension forces in middle
TC – Large Compression forces in middle
Diagonals – Larger forces near ends (tension or compression)

## Slide 49: Questions?