## Slide 1: STANDARD BRIDGE & CULVERT COMPONENTS

## Slide 2: Alberta Bridge Inventory
In Alberta, there are about 13,405 bridges.
Types of bridges in Alberta:
  Standard bridges 3223 (24%)
  Bridge size culverts 8515 (63%) of which (>95% flexible)
  Major bridges 1667 (12%)

## Slide 3: Standard Bridges
Any bridge which is built using standard components and according to standard drawings.
Exception is standard girder bridges with composite decks (e.g. – SMC, SCC, SLC) or pre-stressed girders with overlays (SMO, VSO) which are currently classified as major bridges and must be inspected by a Cl. A.
For inspection purposes standard bridges are divided into two distinct categories:
  Superstructure
  Substructure

## Slide 4: Basic Bridge Components
DECK OR GIRDER TOP
SUPERSTRUCTURE
PIER PART OF
SUBSTRUCTURE
ABUTMENT PART OF
SUBSTRUCTURE
CAP
PILE

## Slide 5: Basic Bridge Components
DECK
SUPERSTRUCTURE
PIER PART OF
SUBSTRUCTURE
ABUTMENT PART OF
SUBSTRUCTURE

## Slide 6: Typical Bridge Components
Superstructure
  It carries the load applied to the deck and transfers it to bridge supports.
Substructure
  It transfers load from the superstructure to the foundation soil or rock.
  It includes all elements below the bearings.

## Slide 7: SUPERSTRUCTURE

## Slide 8: Superstructure for Standard Bridges
Superstructure comprises of bearings and all elements above bearings, including:
  Deck / wearing surface
  Curbs
  Bridgerail
  Girders / stringers
    Timber stringers with timber stripdeck and subdeck.
    Conventionally Reinforced concrete girders.
    Prestressed concrete girders.
  Bearings

## Slide 9: Superstructure Elements
SUB DECK AND STRINGERS ARE
TREATED WITH CREOSOTE.
NOTE:
SPLICE - EXPOSED EDGE
FACES AWAY FROM
APPROACHING TRAFFIC
TIMBER POST
W - BEAM BRIDGERAIL
WHEEL GUARD
STRIP DECK
SUB DECK
TIMBER STRINGERS
TIMBER BLOCK
AT EVERY POST
Timber
Superstructure

## Slide 10: Superstructure Elements
Deck
Provides a smooth & safe riding surface
Transfers load of the deck to other components.
  Three common materials used for the deck:
    Concrete
    Wood
    Steel

## Slide 11: Superstructure Elements
Superstructure
S
u
b
structure
APPROACH
GUARDRAIL
W BEAM
BRIDGERAIL
HAZARD MARKER
CONCRETE CAP
STEEL PIPE PILE
STEEL H - PILE
CURB
CONCRETE
GIRDER
NEOPRENE
BEARING PAD
S
uperstructure
S
u
b
structure
TUBE TYPE
BRIDGERAIL
HAZARD MARKER
CURB
CONCRETE
GIRDER
TIMBER CAP
TIMBER PILE
SPAN 1
SPAN 2
SPAN 1
SPAN 2

## Slide 12: Superstructure Elements
APPROACH RAIL TRANSITION
3.4 mm THICK
THRIE BEAM GUARDRAIL
CONCRETE CAP
STEEL PIPE PILE
STEEL H - PILE
CONCRETE
GIRDER
NEOPRENE
BEARING PAD
SPAN 1
SPAN 2
BRIDGERAIL
GUARDRAIL
3.4 mm THICK
THRIE BEAM GUARDRAIL
2.7 mm THICK W-THRIE BEAM
TRANSITION SECTION
TOP OF FINISHED ROADWAY

## Slide 13: Superstructure Elements
Conventionally Reinforced Concrete Girders
  Concrete is strong in compression and weak in tension.
  Concrete bending members are reinforced with mild reinforcing steel (rebar) to produce reinforced concrete girders.
Prestressed Concrete Girders
  Girders are reinforced with a combination of high-strength steel strand under tension and conventional rebar.
  Girders are designed not to crack.
  Generally, more economical.

## Slide 14: Superstructure Elements
Reinforced Concrete
Girders
TYPE "A" INT.
TYPE "A" CURB
TYPE "G" INT.
TYPE "G" CURB
TYPE "E" INT.
TYPE "E" CURB
2’ – 11 7/8”
16”
28”
22”
2’ – 11 7/8”
16”
3’ – 3”
12”
2’ – 11 7/8”
2’ – 0”
12”
1’ – 6”
2’ – 6”
PRODUCED FROM 1950 TO 1952
LENGTHS: 16’, 20’ & 28’
PRODUCED FROM 1953 TO 1960
LENGTHS: 20’ & 28’
PRODUCED FROM 1952 TO 1965
LENGTHS: 30’, 35’, 40’ & 42’

## Slide 15: Superstructure Elements
Reinforced Concrete
Girders
2’ – 11 7/8”
20”
1’ – 9”
12”
2’ – 11 7/8”
22”
12”
1’ – 9”
TYPE "HC" INT.
TYPE "HC" CURB
TYPE "VH" CURB
PRODUCED FROM 1961 TO 1974
LENGTHS: 20’, 28’, 33’ & 38’
PRODUCED FROM 1974 TO 1979
LENGTHS: 20’, 28’, 33’ & 38’
TYPE “VH" INT.

## Slide 16: Superstructure Elements
Prestressed Concrete
Girders
3’ – 11 1/2”
20”
2’ – 5 3/4”
1’ – 8”
13 3/8”
20”
1206
510
510
340
756
510
PRODUCED FROM 1974 TO 1979
LENGTHS: 20’, 25’, 30’ & 35’
PRODUCED FROM 1979 TO 1990
LENGTHS: 6, 8, 10 & 11 m
TYPE “VS” INT.
TYPE “VS” CURB
TYPE “SM” INT.
TYPE “SM” CURB

## Slide 17: Superstructure Elements
Prestressed Concrete
Girders
CURRENTLY IN USE
LENGTHS: 6, 8, 10, 12 & 14 m
LENGTHS: 6, 8, 10 & 12 m
LENGTHS: 6, 8, 10 & 12 m
1206
510
510
340
356
510
510
1206
350
50
510
1206
350
50
TYPE "SC" INT.
TYPE "SC" EXT.
TYPE "SC" INT.
TYPE "SC" EXT.
TYPE "SL" INT.
TYPE "SL" EXT.

## Slide 18
Superstructure Elements
SLW-510 Curb Unit
SLW-510 Curb and Interior Girders

## Slide 19: Superstructure Elements
SKEW ANGLE
BRIDGE
SKEW ANGLE "LHF"
C
C
BRIDGE
BRIDGE
STREAM

## Slide 20: Superstructure Elements
900
Hazard Marker
  Warning sign at bridge approaches.
  Yellow board with black sloping lines.
  Placed at end of the bridge, in line with railing posts.

## Slide 21: Superstructure Elements
Bearings
  Neoprene or rubber pads or strips.
  Used over steel and concrete caps.
  Transmit all loads from the superstructure to substructure.
  Permit longitudinal movement of the superstructure.
  Allow rotation caused by deflection.

## Slide 22: SUBSTRUCTURE

## Slide 23: Substructure Elements
Substructure comprises of all elements below bearings.
Main components:
Abutments
Pier or Pile Bent (Timber, H pile or Pipe pile pier)
Other components:
Caps & Subcaps
Piles
Sheathing & Bracing
Wingwall
Backwall
Riprap or other scour protection

## Slide 24: Substructure Elements
Substructures can be:
Timber piles with timber cap

## Slide 25: Substructure Elements
Substructures can be:
Timber piles with steel cap

## Slide 26: Substructure Elements
Substructures can be:
Steel “H” piles with steel cap

## Slide 27: Substructure Elements
Substructures can be:
Steel “H” piles with concrete cap
Steel pipe piles with concrete cap

## Slide 28: Substructure Elements
SPILL THROUGH ABUTMENT
HIGH BACKWALL ABUTMENT
ABUTMENT CAP
CAP SPLICE
TIMBER SCAB
BACKWALL
HEAVY ROCK
RIPRAP
WINGWALL
WINGWALL
PILE
ABUTMENT SUBCAP
ANCHOR PILES
ABUTMENT PILES

## Slide 29: Substructure Elements
Timber Piers ( 2 Types
Of Bracing)
PIER CAP
CAP SPLICE
SUB CAP
WITH SWAY BRACING
WITH PLANKING
STRUTS
MAXIMUM HEIGHT FOR A
SINGLE ROW OF PILING IS 3.0 m

## Slide 30: Substructure Elements
Substructures Pier Supports:
Timber Sway bracing
Full Timber Sheathing

## Slide 31: Substructure Elements
Substructures Pier Supports:
Steel Bracing

## Slide 32: Substructure Elements
DECK SURFACE
STEEL NOSE
STEEL BRACING
GALVANIZED STEEL
H-PILES
HIGH BACKWALL ABUTMENT
PIER
(HALF VIEW ONLY)
(HALF VIEW ONLY)
STEEL CAP
STEEL H PILE SCAB
STREAM BED
3.0 m MAX.
6.0 m MAX.

## Slide 33: Substructure Elements
STEEL CAP
TIMBER PILES
SPILL THROUGH ABUTMENT
PIER
HALF VIEW ONLY
HALF VIEW ONLY
DECK SURFACE
PLANK SHEATING
WINGWALL PILE
STEEL CAPITAL
STREAM BED
3.5 m MAXIMIM
1.25 m MAXIMIM

## Slide 34: Substructure Elements
(HALF VIEW ONLY)
(HALF VIEW ONLY)
PIER
ABUTMENT
DECK SURFACE
GALVANIZED STEEL
H-PILES
GALVANIZED PIPE
PILES
CONCRETE WINGWALL
CONCRETE PIER CAP
STREAM BED
1.0 m
MAX
6.0 m
MAX

## Slide 35: Substructure Elements
2.5 m
MAX
SL PRESTRESSED CONCRETE GIRDER BRIDGE WITH STEEL SUBSTRUCTURE
HIGH ABUTMENT BACKWALL (ELEVATION)
GALVANIZED STEEL
H-PILES
GALVANIZED STEEL CAP WITH STIFFENERS OVER PILES

## Slide 36: Substructure Elements
SL PRECAST GIRDER BRIDGE WITH STEEL SUBSTRUCTURE (SECTION)
GALVANIZED STEEL CAP
HP 310 X 94
T.T NAILING STRIP
BOLTED TO PILE
T.T PLANKING
FILTER FABRIC
SL GIRDER
DOWEL
NEOPRENE PAD
GALVANIZED STEEL PILE
HP 310 X 94
C
ABUT. &
PILES

## Slide 37: Substructure Elements
SL PRECAST GIRDER BRIDGE WITH STEEL SUBSTRUCTURE PIER (ELEVATION)
GALVANIZED STEEL CAP WITH STIFFENERS OVER PILES
STEEL NOSE
U/S
PILE
BRACING
GALVANIZED STEEL
PILES
5.5 m
MAX
2.5 m
MAX

## Slide 38: Substructure Elements
SL PRECAST GIRDER BRIDGE WITH STEEL SUBSTRUCTURE PIER (ELEVATION)
GALVANIZED STEEL CAP
2 - HP 310 X 94 C/W STIFFENER
PLATES
SL GIRDER
DOWEL
NEOPRENE PAD
GALVANIZED STEEL PILE
HP 310 X 94
C
PIER
PILES
SL GIRDER
ASPHALT
FIBRE BOARD

## Slide 39
CULVERTS

## Slide 40: Culvert Components
CULVERT
ROADWAY
STREAMBED (U/S)
CONCRETE SHOULDER
(OR COLLAR)
CONCRETE HEADWALL
CONCRETE
CUT-OFF WALL
BARREL SECTION
BEVEL END
BEVEL END
U/S INVERT
CLAY SEAL
(BOTH ENDS)
INLET
OUTLET
RIPRAP
STREAMBED (D/S)
D/S INVERT
APRON
CROWN OF ROAD
LONGITUDINAL SECTION THROUGH CULVERT
C

## Slide 41: Culvert Components
SPAN
RISE
ROAD SURFACE
CULVERT
TOP PLATES
(ROOF OR TOP ARC)
SIDE PLATES
(WALL OR SIDE ARC)
BOTTOM PLATES
(FLOOR OR BOTTOM ARC)
INVERT
SECTION
C

## Slide 42: Culvert Components
COLLAR
HEADWALL
APRON
INVERT
CUT-OF-WALL
COLLAR
HEADWALL
CUT-OF-WALL

## Slide 43: Typical Inlet Configurations
SQUARE FLUSH
INLET
SQUARE PROJECTING
INLET
BEVEL FLUSH
INLET
BELL-MOUTH
INLET (PLAN)
flow

## Slide 44: Concrete End Treatment
H1
H2
SEEPAGE
F
Uplift force, F is proportional to H1 – H2
Seepage is proportional to H1 – H2

## Slide 45: Concrete End Treatment
w
F
Headwall
Collar
Cut-off-wall

## Slide 46: Concrete End Treatment
Concrete end treatment has five important functions:
  Weight provides downward force to resist uplift.
  Cut-off wall lengthens the seepage path.
  Collar strengthens the bevel edges.
  Enhances the inlet transition.
  Aesthetics.

## Slide 47: Clay Seals
Problems due to seepage:
Fine material is removed from the granular backfill.
  Loss of material creates voids.
  Support length of the backfill is reduced.
  Culvert can deform.
Uplift forces are increased.

## Slide 48: Clay Seals
CLAY SEAL (EACH END)

## Slide 49: Scour Protection - Aprons
Flowing water causes shear forces on the bed.
Shear force is proportional to velocity.
High shear forces will erode bed and bank material.
  Causes fill stability problems at inlet and outlet.
  Causes structural deformation.

## Slide 50: Scour Protection - Aprons
Riprap is placed to protect the end of culverts.
Larger and heavier riprap provides higher shear resistance.
Cut-off wall helps anchor riprap.

## Slide 51
Culvert (SPCSP) Installation

## Slide 52
Culvert (CSP) Installation

## Slide 53
Culvert (CSP) Installation

## Slide 54
Culvert (CSP) Installation

## Slide 55
SPCSP Culvert Grade Separation

## Slide 56
SPCSP Arch Culvert – Wildlife Overpass

## Slide 57
SPCSP VE Arch Culvert – Pedestrian Underpass

## Slide 58: Questions?